## Slide 1: Computer Architecture and organization M.Nivedita Assistant Professor SCOPE VIT Chennai

## Slide 2: Books
David A. Patterson and John L. Hennessy, Computer Organization and Design -The Hardware / Software Interface 6th Edition, Morgan Kaufmann, 2020.
Computer Architecture and Organization-Designing for Performance, William Stallings, Tenth edition, Pearson Education series, 2016 .
Carl Hamacher, Zvonko Vranesic, Safwat Zaky, Computer organization, Mc Graw Hill, Fifth edition, Reprint 2011.

## Slide 3: Assesment
CAT – I - 15
CAT – II - 15
Digital ASSIGNMENT - 30
Term End Exam - 40

## Slide 4: Objective
How computers work, basic principles.
How to analyze their performance.
How computers are designed and built.
To teach arithmetic of computers.
To provide knowledge of memory technologies, interfacing techniques and subsystem devices and the issues in that.

## Slide 5: Motivation
This knowledge will be useful if you need to
Design/build a new version of a computer
Improve software performance
Purchase a computer
Provide a solution with an embedded computer

## Slide 7: What is computer architecture?
Computer architecture deals with the functionality of every hardware unit of a CPU. i.e. what a specific hardware unit works in a computer
Computer architecture is a specification detailing how a set of software and hardware technology standards interact to form a computer system or platform.

## Slide 8: What is computer Organization?
Computer organization deals with the implementation of every hardware unit of a CPU. i.e. how a specific hardware unit works in a computer
It refers to the operational units of the hardware device and interconnections between various hardware devices realize the architectural specifications.

## Slide 10
All Intel x86 family will share the same basic architecture.
The IBM System/370 family will share the same basic architecture.
This helps to enable code compatibility.(backwards)
But organisation is different for different versions.

## Slide 11
Applications
Technology
Interfaces
ISA
API
Link
I/O Chan
Machine Organization
Regs
IR
Measurement &
Evaluation
Computer Architect

## Slide 12: Structure and Function
Structure is the way in which components relate to each other.
Function is the operation of individual components as part of the structure. The computer functions are,
  Data processing
  Data storage
  Data movement
  Control

## Slide 13: Functional View
Data Movement
apparatus
Control Mechanism
Data Storage
Facility
Data Processing Facility
Operating Environment (Source, Destination of Data)

## Slide 14: Data Movement
movement
control
Storage
Processing

## Slide 15: Storage
Movement
Control
Storage
Process

## Slide 16: Processing from/to storage
Movement
Control
Storage
Process

## Slide 17: Processing from storage to I/O
Movement
Control
Storage
Process

## Slide 18: Structure
Storage
Processing
Computer
Peripherals
Communication Lines

## Slide 19: Structure - Top Level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 20: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 21: Structure - The Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Login
Control
Unit
ALU
Registers
Internal
Bus
Control Unit

## Slide 22: Structural components
CPU – Processor
Main Memory – Stores data
I/O – Moves the data
System Interconnection
Control Unit – controls operation
ALU – data processing
Registers – storage internal to CPU
CPU Interconnection

## Slide 23: ENIAC
  ENIAC (Electronic Numerical Integrator And Computer)
  1st general-purpose electronic digital computer.
  Designed by John Mauchly and John Presper Eckert at University of pennsylvania.
  Funded by US BRL (Ballistic Research Lab) to develop range and trajectory tables for new weapons
    Until then, BRL employeed more than 200 people who, using desktop calculators to solve the necessary ballistics equations
  The proposal accepted in 1943, the machine completed in 1946, and dismantled in 1955
  Characteristics
    30 tons, 15000 square feet, 18000 vacuum tubes, 140 KW power dissipation
    Decimal machine
      20 accumulators each holding 10-digit decimal number
      Each digit is represented by a ring of 10 vacuum tubes
      5,000 additions per second
    Manually programmed by setting switches and plugging/unplugging cables

## Slide 24: ENIAC

## Slide 25: Von Neumann Machine
The task of entering and altering programs for the ENIAC was extremely tedious.
The programming process could be facilitated if the program could be represented in a form suitable for storing in memory alongside the data.
Then, a computer could get its instructions by reading them from memory, and a program could be set or altered by setting the values of a portion of memory.

## Slide 26: The Stored Program Concept
Von Neumann’s proposal was to store the program instructions right along with the data
The stored program concept was proposed about fifty years ago; to this day, it is the fundamental architecture that fuels computers.

## Slide 27: von Neumann/Turing
Stored Program concept
Main memory storing instructions and data
ALU operating on binary data
Control unit interpreting instructions from memory and executing
Input and output equipment operated by control unit
Princeton Institute for Advanced Studies
  IAS
Completed 1952

## Slide 28: The Von Neumann Machine & IAS

## Slide 29: Structure of IAS Computer

## Slide 30: The Stored Program Concept and its Implications
The Stored Program concept had several technical ramifications:
  Four key sub-components operate together to make the stored program concept work
  The process that moves information through the sub-components is called the “fetch execute” cycle
  Unless otherwise indicated, program instructions are executed in sequential order

## Slide 31: Four Sub-Components
There are four sub-components in von Neumann architecture:
  Memory
  Input/Output (called “IO”)
  Arithmetic-Logic Unit
  Control Unit
While only 4 sub-components are called out, there is a 5th, key player in this operation: a bus, or wire, that connects the components together and over which data flows from one sub-component to another
Let’s look at each sub-component in more detail …

## Slide 32: Memory
As you already know, there are several different flavors of memory
Each type of memory represents cost/benefit tradeoffs between capability and cost .

## Slide 33: Memory Types: RAM
RAM is typically volatile memory (meaning it doesn’t retain voltage settings once power is removed)
RAM is an array of cells, each with a unique address
A cell is the minimum unit of access. Originally, this was 8 bits taken together as a byte. In today’s computer, word-sized cells (16 bits, grouped in 4) are more typical.
RAM gets its name from its access performance. In RAM memory, theoretically, it would take the same amount of time to access any memory cell, regardless of its location with the memory bank (“random” access).

## Slide 35: Memory Types: ROM
It gets its name from its cell-protection feature. This type of memory cell can be read from, but not written to.
Unlike RAM, ROM is non-volatile; it retains its settings after power is removed.
ROM is more expensive than RAM, and to protect this investment, you only store critical information in ROM …

## Slide 36: ROM (Read Only Memory)
Types of ROM:
  Programmable ROM, where the data is written after the memory chip has been created. It is non-volatile.
  Erasable Programmable ROM, where the data on this non-volatile memory chip can be erased by exposing it to high-intensity UV light.
  Electrically Erasable Programmable ROM, where the data on this non-volatile memory chip can be electrically erased using field electron emission.

## Slide 38: Memory Types: Registers
There is a third, key type of memory in every computer – registers.
Register cells are powerful, costly, and physically located close to the heart of computing.
Registers are the main participants in the fetch execute cycle.

## Slide 39: Memory Types: Other
Modern computers include other forms of memory, such as cache memory.
Remember, memory types exist at different trade offs.

## Slide 40: I/O: Input and Output
There is both a human-machine interface and a machine-machine interface to I/O.
  Examples of the human-machine interface include a keyboard, screen or printer.
  Examples of the machine-machine interface include things like mass storage and secondary storage devices.
Input and output devices are the least standardized of the various sub-components, which means that you have to pay extra special attention to make certain that your input or output devices are compatible with your machine.

## Slide 41: The ALU
The third component in the von Neumann architecture is called the Arithmetic Logic Unit.
This is the subcomponent that performs the arithmetic and logic operations for which we have been building parts.
The ALU is the “brain” of the computer.
It contains the circuitry to perform addition, subtraction, multiplication and division, as well as logical comparisons (less than, equal to and greater than).

## Slide 42: Control Unit
The last of the four subcomponents is the Control Unit.
The control unit drives the fetch and execute cycle.
Controls which address is loaded into the memory and what operation is taking place in the data.

## Slide 43: IAS - details
The memory of the IAS consists of 1000 storage locations, called words, of 40 binary digits each.
Both data and instructions are stored there.
Each number is represented by a sign bit and a 39-bit value.
A word may also contain two 20-bit instructions, with each instruction consisting of an 8-bit operation code specifying the operation to be performed and 12-bit address designating one of the words in memory.

## Slide 44: IAS Memory Formats
NUMBER WORD
Sign Bit
39
0
1

## Slide 45: Instruction Word
0
39
28
20
8
Left Instruction
Right Instruction
Opcode
Opcode
Address
Address

## Slide 46
Set of registers (storage in CPU)
  Memory Buffer Register
  Memory Address Register
  Instruction Register
  Instruction Buffer Register
  Program Counter
  Accumulator
  Multiplier Quotient

## Slide 47: Expanded Structure of IAS Computer

## Slide 48: Registers
MBR – Memory Buffer Register contains a word to be stored in memory or sent to the I/O unit or is used to receive a word from memory.
MAR – Memory Address Register specifies the address of the word to be written from MBR, to be read into MBR.
Instruction Register (IR) - 8 bit opcode instruction being executed.
Instruction Buffer Register (IBR)– hold the right hand instruction from a word in memory.
Program Counter(PC) – address of the next instruction pair fetched from memory.

## Slide 49: Contd.,
Accumulator (AC) , Multiplier Quotient (MQ)
temporarily hold operands and the results of
ALU operations
Example:
40 bit multiply operation
Most Significant Bit - AC
Least Significant Bit - MQ

## Slide 50: CONTD.,
IAS – Instruction Cycle
Subcycles
 Fetch cycle
 Execute cycle
Fetch cycle
Opcode of next instruction is loaded in IR
Address portion is loaded in MAR
Instruction taken from IBR or can be obtained from memory (MBR)

## Slide 51: Contd.,
Execute cycle
Once the opcode is in IR the execute cycle is performed
Control circuitry interprets the opcode and executes instruction by sending out control signals, which allows Data movement or operation to be performed by ALU.

## Slide 52
=1
=1
=1
LOAD M(X),500
ADD M(X),501
LOAD M(X),500
ADD M(X),501
EXAMPLE

## Slide 53
500
500
3
MBR=3
3
=3
EXAMPLE

## Slide 54
ADD M(X)
501
501
4
MBR =4
PC=2
EXAMPLE

## Slide 55
MAR = 2
2
STOR M(X) 500, (Other Ins)
STOR M(X),500
Other Ins
EXAMPLE

## Slide 56
MAR = 500
500
7
EXAMPLE

## Slide 64: IAS Instruction Set
Data Transfer – moves the data between Memory and ALU
registers or between two ALU registers
Unconditional Branch – CU executes instructions in sequence from memory, sequence can be changed by branch instructions (repetitive operations)
Conditional Branch – branch can be made dependent on condition.
Arithmetic – operations performed by ALU
Address modify – permits the address to be computed in the ALU and then inserted into instructions stored in memory.

## Slide 66: Harvard Architecture
Finished at Harvard University in 1947.
It wasn't so modern as the computer from von Neumann team. But it introduced a slightly different architecture.
Memory for data was separated from the memory for instruction. This concept is known as the Harvard architecture.

## Slide 67: Diagrammatic view of Harvard Architecture

## Slide 68: Advantages of Harvard
since it has two memories , this allows parallel access to data and instructions.
Development of the Control Unit is expensive and needs more time
Data and instructions are accessed the same way.
Both memories can use different cell sizes.

## Slide 69: Disadvantages of Harvard
Free data memory cant be used for instruction and vice-versa.
Production of a computer with two buses is more expensive and needs more time.

## Slide 71: Harvard vs von Neumann
Harvard
Two memories with two Buses allow parallel access to data access and instructions.
Control unit for two buses is more complicated and more expensive.
Both memories can use different sizes.
Von Neumann
Content of the memory if organised and all installed memory can be used.
One bus is simpler for the control unit design
Computer with one bus is cheaper.

## Slide 72: Harvard vs von Neumann
Harvard
Development of a complicated Control Unit needs more time.
Free data memory can’t be used for instruction and vice-versa.
Von Neumann
Development of the Control Unit is cheaper and faster.
Data and instruction is accessed in the same way.
One Bus ( for Data, instruction and devices) is a bottleneck.

## Slide 73: RISC and CISC Architectures

## Slide 74: RISC (Reduced Instruction Set Computer)
A Reduced Instruction Set Computer is a type of microprocessor architecture that utilizes a small, highly-optimized set of instructions rather than the highly-specialized set of instructions typically found in other architectures.
Examples of RISC processors: IBM RS6000, MC88100; DEC’s Alpha 21064, 21164 and 21264 processors
It is a highly customized set of instructions used in portable devices due to system reliability such as Apple iPod, mobiles/smartphones, Nintendo DS

## Slide 75: RISC Features
RISC processors use a small and limited number of instructions.
RISC machines mostly uses hardwired control unit.
RISC processors consume less power and are having high performance.
Each instruction is very simple and consistent.
RISC processors uses simple addressing modes.
RISC instruction is of uniform fixed length.

## Slide 76: CISC (Complex Instruction Set Computer)
A complex instruction set computer (CISC) is a computer architecture in which single instructions can execute several low-level operations (such as a load from memory, an arithmetic operation, and a memory store) or are capable of multi-step operations or addressing modes within single instructions.
Examples of CISC processors are: Intel 386, 486, Pentium, Pentium Pro, Pentium II, Pentium III ; Motorola’s 68000, 68020, 68040, etc.
It has a large collection of complex instructions that range from simple to very complex and specialized in the assembly language level, which takes a long time to execute the instructions.

## Slide 77: CISC Feature
CISC chips have a large amount of different and complex instructions.
CISC machines generally make use of complex addressing modes.
Different machine programs can be executed on CISC machine.
CISC machines uses micro-program control unit.
CISC processors are having limited number of registers.

## Slide 78
CISC Multiplication
  MULT 1:2,2:1

## Slide 79: CISC vs RISC
CISC uses a large set of complex machine language instructions, while RISC uses a reduced set of simpler instructions
The primary difference between RISC and CISC architecture is that RISC-based machines execute one instruction per clock cycle. In a CISC processor, each instruction performs so many actions that it takes several clock cycles to complete.