## Slide 1: Instruction
Instruction is a statement by which the operation of CPU is determined.
These instructions referred as “Machine instructions or computer Instructions”
Elements of Machine instruction
  Operation code
  Source operand reference
  Result operand Reference
  Next instruction reference

## Slide 2: Instruction Sets
The collection of different instructions that the CPU can execute is referred to as the CPU’s instruction set.
Design Issues of Instruction Sets
  Operation repertoire
  Operand Reference
  Length of Instruction
  Data Types

## Slide 3: Instruction Representations
Each instruction is represented by sequence of bits
The instruction is divided into two fields
  Opcode field
  Operand field
This operand field further divided into one to four fields.
This layout of the instruction is known as the “Instruction Format”
Simple instruction format
Opcode
Operand
Address1
Operand
Address2
Result
Address1
Next
Instruction

## Slide 4: Instruction Set Types
Instruction Set is categorized into types based on
  Operation performed,
  number of operand addresses
  and addressing modes.

## Slide 5: Instruction Set category Based on Operation
Data movement instructions: Move data from a memory location or register to another memory location or register without changing its form.
  Memory
    LOAD, STORE, MOV
  I\O Instructions
    IN, OUT

## Slide 6: Instruction Set category Based on Operation
Data Processing Instructions: Arithmetic and logic (ALU) instructions - Changes the form of one or more operands to produce a result stored in another location
  Arithmetic
    Add, Sub, MUL
  logic Instructions
    AND, OR, ..

## Slide 7: Instruction Set category Based on Operation
Control Instructions :Any instruction that alters the normal flow of control from executing the next instruction in sequence
  Conditional
    JNZ, JZ, JNP,JNN…..
  Un Conditional
    Jump

## Slide 8: 4-,3-,2-,1-,and 0- address instructions
Instruction Set categorized into four categories based on number of operand address in the instruction.
  4- Address Instruction
  3-Address Instruction
  2-Address Instruction
  1-Address Instruction
  0-Address Instruction

## Slide 9: Basic Instruction Types
C=A+B
How is this high-level language command implemented in the computer?
To carry out the action
C  [A]+[B]
the contents of memory locations A and B are fetched from memory and transferred into the processor, where their sum is computed and then transferred to memory location C

## Slide 10: 4- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
NextiAddr
8
24
24
24
24
+
CPU
Op1
Op2
Resop
Example: add M1,M2,M3, nexti
M(1)M(2)+M(3)
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
NextiAddr=1
Total=5
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 5 + 3 =8

## Slide 11: 3- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
8
24
24
24
+
CPU
Op1
Op2
Resop
Example: add M1,M2,M3
M(1)M(2)+M(3)
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
Total=4
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 4+ 3 =7
PC
24

## Slide 12: 2- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
Op2Addr
8
24
24
+
CPU
Op1
Op2
Resop
Example: add M2,M3
M(2)M(2)+M(3)
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
Total=3
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 3+ 3 =6
PC
24

## Slide 13: Two-Address Instruction
An Add instruction: Add A, B performs the operation A[A]+[B]. When the sum is calculated, the result is sent to memory and stored in location A, replacing the original contents of this location.
C  [A]+[B] can be implemented as
Move C, B
Add C,A

## Slide 14: 1- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
8
24
+
CPU
Op1
Op2
Resop
Example: add M2
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Total=2
To Execute an Instruction
Op1=1
Total=1
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 2+ 1 =3
PC
24
Acc

## Slide 15: One-Address Instruction
Examples:
Add A means: Add the contents of memory location A to the contents of the accumulator register and place the sum back into the accumulator
Move A means: Copy the contents of memory location A to the accumulator register
Store A means: Copy the contents of the accumulator register to memory location A
General form: Operation Source

## Slide 16: One-Address Instruction
Thus, C  [A]+[B] can be implemented as
(Assembly Language)
Move A
Add B
Store C
which means (Register Notation):
Accumulator  [A]
Accumulator  [Accumulator] + [B]
C  [Accumulator]

## Slide 17: 0-Address Instruction

## Slide 18: Evaluate a = (b+c)*d - e
ab+c
add a, b, c
mul a, a, d
sub a, a, e
aa*d
aa-e
ab
load a, b
add a, c
mul a, d
aa+c
aa*d
sub a, e
aa-e
Accb
load b
add c
mul d
AccAcc+c
AccAcc*d
sub e
AccAcc-e
store a
aAcc
push e
push d
push c
mul
sub
pop a
3-Address
2-Address
1-Address
0-Address
push b
add

## Slide 19
3-ADDRESSMACHINE Add R1, B, C Add R2, D, E Mul A, R1, R2 | 2-ADDRESSMACHINE Load R1, B Add R1, C Load R2, D Add R2, E Mul R2, R1 Store A, R2 | 1-ADDRESSMACHINE Load B Add C Store Temp Load D Add E Mul Temp Store A | 0-ADDRESSMACHINE Push B Push C Add Push D Push E Add Mul Pop A
Write code to implement the expression: A= (B + C) * (D + E)on
3-, 2-, 1- and 0-address machines. In accordance with programming
language practice , computing the expression should not change
the values of its operands.
Ans.

## Slide 20: Addressing Modes
The way the operands are chosen during the program execution is dependent on the addressing mode of the instruction.
The term addressing modes refers to the way in which the operand of an instruction is specified. Information contained in the instruction code is the value of the operand or the address of the result/operand.

## Slide 21: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack
Notes: 2

## Slide 22: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD 5
  Add 5 to contents of accumulator
  5 is operand
No memory reference to fetch data
Fast
Limited range
Notes: 3

## Slide 23: Immediate Addressing Diagram
Operand
Opcode
Instruction
Notes: 4

## Slide 24: Direct Addressing
Address field contains address of operand
Effective address (EA) = address field (A)
e.g. ADD A
  Add contents of cell A to accumulator
  Look in memory at address A for operand
Single memory reference to access data
No additional calculations to work out effective address
Notes: 5

## Slide 25: Direct Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Notes: 6

## Slide 26: Indirect Addressing (1)
Memory cell pointed to by address field contains the address of (pointer to) the operand
EA = (A)
  Look in A, find address (A) and look there for operand
e.g. ADD (A)
  Add contents of cell pointed to by contents of A to accumulator
Notes: 7

## Slide 27: Indirect Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Pointer to operand
Notes: 9

## Slide 28: Indirect Addressing (2)
Large address space
May be nested, multilevel, cascaded
  e.g. EA = (((A)))
    Draw the diagram yourself
Multiple memory accesses to find operand
Hence slower
Notes: 8

## Slide 29: Register Addressing (1)
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch
Notes: 10

## Slide 30: Register Addressing (2)
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
Notes: 11

## Slide 31: Register Addressing Diagram
Register Address R
Opcode
Instruction
Registers
Operand
Notes: 12

## Slide 32: Register Indirect Addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space
One fewer memory access than indirect addressing
Notes: 13

## Slide 33: Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Notes: 14

## Slide 34: Relative Addressing
A version of displacement addressing
R = Program counter, PC
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
Notes: 17

## Slide 35: Indexed Addressing Mode
A holds base address
R holds displacement, may be explicit or implicit (segment registers in 8086)
Content of the index register is added to the address part of the instruction to obtain effective address of the operand.
EA = A + (SI)
Ex: Mov CX, [SI] 2400H
Advantage: Flexibility
Disadvantage: Complexity

## Slide 36: Base Register Addressing Mode
The content of the base register is added to the address part of the instruction to obtain the effective address of the operand.
EA = A + (BX)
Ex: Mov 2345H [BX], 0AC24H
Advantage: Flexibility
Disadvantage: Complexity

## Slide 37: Stack Addressing
Operand is (implicitly) on top of stack
e.g.
  ADD Pop top two items from stack and add
Notes: 21

## Slide 38: Auto Increment and Auto Decrement Addressing Modes
This addressing mode is used when the address stored in the register refers to a table of data in memory, it is necessary to increment or decrement the register after every access to the table.
Ex: Add R1, (R2)+
R1 <- R1+R2
R2 <- R2+1
Add R1,-(R2)
R2<- R2-1
R1<- R1+R2